PART 1:
PODEM:
- getObjective:
- This function tries to activate the fault by checking if it is activated or not. Returns a true.
- If the fault is activated, D-frontier is updated. If D-frontier is empty, false is returned.
- First gate from the D-frontier is chosen and its first LOGIC_X on its inputs and is set to objective gate. The non-controlling value of the gate from D-frontier is set to objective value. Then it returns a true.
- updateDFrontier:
- Using the gate number, each gate is evaluated by checking its inputs for a LOGIC_D or LOGIC_DBAR, and output for a LOGIC_X.
- backtrace:
- It sets the PIs so that the fault location is set to the objective value.
We have tested the algorithm using the .fault files shown below. We compared the output files with the reference output provided and they matched correctly.
PART 2:
EVENT DRIVEN SIMULATION:
- Used a queue to store gates. Each gate from the queue is evaluated to obtain an output with its current inputs.
- If the output value of the gate changes, its output gates are pushed into the queue one after the other. The process continues until the queue is empty.
- The difference in run times with and without event driven simulation can be observed below. We used the fault lists provided to test and compare the algorithm.
Charts showing the difference in running times of PODEM for Part 1, Part 2:
Fault list	Part 1(mm:sec:ms)	Part 2(mm:sec:ms)
ex1.fault	0:00.02	0:00.02
ex2.fault	0:00.02	0:00.02
c17.fault	0:00.02	0:00.02
c432.smallfault	0:12.40	0:05.85
c432.medfault	0:53.71	0:24.78
c432.bigfault	34:03.15	4:56.79

Fault list	Part 2(mm:sec:ms)	Part 3(mm:sec:ms)
ex1.fault	0:00.02	0:00.02
ex2.fault	0:00.02	0:00.01
c17.fault	0:00.02	0:00.03
c432.smallfault	0:05.85	0:00.02
c432.medfault	0:24.78	0:00.33
c432.bigfault	4:56.79	3:46.42